## Slide 1
DHT11
List Component | DHT11 Sensor | ESP32 GPIO | Wire Color
1. ESP32 V4 (38 Pin GPIO) | VCC | 3.3V | 
2. DHT11 | GND | GND | 
3. Arduino IDE | DATA | GPIO27 | 
4. Breadboard |  |  | 
5. Jumper Male to Male |  |  | 
Wiring Diagram
ESP32

## Slide 2
Topic:
- /esp32-mqtt/temp
- /esp32-mqtt/humi
Publish:
Subscribe:
MQTT Client
MQTT Client
MQTT Broker
Topic:
- /esp32-mqtt/temp
- /esp32-mqtt/humi
broker.mqtt-dashboard.com
Publish:
Publisher
Subscriber
MQTT Protocol Architecture
MQTT is an OASIS standard messaging protocol for the Internet of Things (IoT). It is designed as an extremely lightweight publish/subscribe messaging transport that is ideal for connecting remote devices with a small code footprint and minimal network bandwidth. MQTT today is used in a wide variety of industries, such as automotive, manufacturing, telecommunications, oil and gas, etc.
MQTT (Message Queueing Telemetry Transport )

## Slide 3
Node-RED Installation
Cara Install Node-RED pada Windows
1. Install Node.js
1). Link: https://nodejs.org/en/
2). Download Node.js versi LTS
terbaru dan Install
2. Install Node-RED
1). Buka CMD/Terminal
2). Pastikan Laptop/PC tersambung ke koneksi Internet
3). Copy dan Paste command berikut pada CMD/Terminal :
4). Tunggu sampe proses instalasi selesai
npm install -g --unsafe-perm
node-red
3. Run Node-RED
1). Tulis command berikut
pada CMD/Terminal :
2). Biarkan CMD/Terminal Berjalan
3). Buka Browser dan akses url link berikut :
Node-RED Editor: http://127.0.0.1:1880
Node-RED Dashboard :
http://127.0.0.1:1880/ui
node-red
Node-Red merupakan salah satu alat pemrograman (programming tools) yang dapat menghubungkan perangkat keras (hardware), API, dan layanan online dengan cara yang sangat mudah dan menarik.

## Slide 4
DHT11 Dashboard